# Functional Test Record
Marshall Taylor
8/21/2015
HW version v02
## Testing with I2C mode
#### Test the I2C Addressing
Procedure:
1. Use ReadAllData sketch with default HW
2. Test default condition
3. Switch address jumper
4. Change address in code
5. Test alternate address
Criteria:
1. Did the modes work? YES
2. Does the silkscreen match the operation? YES
#### Signal Integrity of I2C lines
Procedure:
1. Attach scope probes to SDA and SCL with the shortest wire possible
2. Capture a full operation
3. Capture a zoom of 3 consecutively toggling SDA bits
Criteria:
1. Are I2C interface rise times are far below clk pulse high width?
2. Record the pullup resistor value as measured:
- 1: 4.692 kOhm
- 2: 4.698 kOhm

## Testing with SPI mode
Procedure:
1. Connect the BME280 to an arduino through the level shifter
2. Attach scope probes to MOSI, MISO, CS, and CLK on the BME280 side
3. Capture a full operation
4. Capture a zoom of 3 consecutively toggling data bits for MISO
5. Capture a zoom of 3 consecutively toggling data bits for MOSI
Criteria:

1. Does the clock phase and polarity match the datasheets? YES, phase defined by clk state after SS goes low
2. Include the captures.

## Power Consumption
Procedure:
1. Measure the current draw before the IC is configured
2. Configure and spam read the data
3. Measure the current draw during spam read
Criteria:
1. Are both numbers below 5mA?
2. Record both currents
- Idle: ~1.5mA
- Max: ~2.0mA